## Slide 1: Demonstration – Data plotting

## Slide 2: Python Standard Testing Application
Marc Eitner, Palash Jain, and Chloe Johnson
ME 369
Dr. Mitchell Pryor
PySTA

## Slide 3: Outline
Overall Objective
Goal of Project
Demonstration
Code Development
  Signal Reading
  GUI
  Animation
Future Work

## Slide 4: Overall Objective
Replicate an instrument interface such as LabVIEW using Python and a Raspberry Pi, making data collection for small experiments portable, affordable, and user-friendly.
LabVIEW can be large and expensive
  Software: $400 - $5000 /year
  Data Acquisition: > $200
PySTA
  Python: FREE
  Data Acquisition:
    Raspberry Pi:
    Analog to Digital Converters: $2.50

## Slide 5: Goal of Project
y(t)
a(t)
Raspberry Pi
GUI in PyQT
Store Data
Live Voltage Outputs
Beam Animation

## Slide 6: Hardware wiring
Connection of Analog-Digital-Converter
https://cdn-shop.adafruit.com/datasheets/MCP3008.pdf
Analog sensor connection side
Raspberry Pi connection side

## Slide 7: Code Development: Signal Reading 1
Main library used: Adafruit_MCP3008 and SPI.SpiDev
Interface between Analog-Digital-Converter (MCP3008) and Raspberry Pi
Create an object:
mcp = Adafruit_MCP3008.MCP3008(spi=SPI.SpiDev(SPI_PORT,SPI_DEVICE))
…and read the data:
for i in range(0,8): # loop over all channels
values[i] = mcp.read_adc(i)*3.3/1024 # read and convert to Volts

## Slide 8: Code Development: Signal Reading 2
Class Measurement():
def __init__(self, fs=100):
self.time = []
self.data = []
self.fs = fs
def setData(self, values)
def setTime(self, t0)
def saveData(self, data_type = ‘time_domain’, ‘name = testdata’)
def filterData(self, filter_options) future work

## Slide 9: GUI: The PyQt5 Library
Three major actions in PyQt5
Create Widgets
Qlabel()
QLineEdit()
QPushButton()
QCheckBox()
QHBoxLayout()
QVBoxLayout()
QGridLayout()
FigureCanvas()
and many others…
Place Widgets
layout.addWidget (widget)
addLayout(layout)
setLayout(layout)
addTab()
…
Feedback Action
button.clicked.connect (function)
textChanged.connect (function)
checkbox.stateChanged.connect(function)
…

## Slide 10: GUI: Initialization Pane

## Slide 11: GUI: Configuration tab

## Slide 12: GUI: Plots tab

## Slide 13: GUI: Animation tab

## Slide 14: Code Development: GUI
Initialization Panel

## Slide 15: Code Development: GUI
Initialization Panel

## Slide 16: Code Development: GUI
Initialization Panel

## Slide 17: Code Development: GUI
Initialization Panel

## Slide 18: Code Development: GUI
Initialization Panel

## Slide 19: Code Development: GUI

## Slide 20: Code Development: GUI
plot_in_gui.py

## Slide 21: GUI: Animation tab

## Slide 22: Code Development: GUI
beam_animate_in_gui.py

## Slide 23: Code Development: Animation

## Slide 24: Code Development: Animation

## Slide 25: Code Development: Animation

## Slide 26: Code Development: Animation
Simulated Voltage Outputs:
Simulated Beam Displacement Animation:

## Slide 27: Code Development: Animation
Simulated Voltage Outputs:
Simulated Beam Displacement Animation:

## Slide 28: Future Work
Saving data to file in the GUI
Interfacing setup with hydraulic servos

## Slide 29
Questions or Comments?